## Slide 1
Alloy Lab Database
Stage 2 — Characterization Pipelines & Database Integration
Progress review

## Slide 2
Stage 2 — Goal and Status at a Glance
Turn three characterization techniques (XRD, VSM, SEM) into validated, database-integrated pipelines — feeding a future ML-based composition/synthesis model.
XRD
Complete
VSM
Complete
SEM
In progress — real, scoped challenge
Database integration
Complete for XRD + VSM
Element-fraction table
Core built; auto-wiring deferred
Standalone interactive tools
XRD + VSM done; SEM in progress
Alloy Lab Database — Stage 2
1

## Slide 3
XRD — Complete
Full analysis pipeline: background subtraction, Kα2 stripping, peak fitting, R² fit quality, Scherrer crystallite size, d-spacing, doublet detection
  Validated against a certified reference standard (NIST LaB6) — lattice parameter within 0.0001 Å
Database schema + real production integration
  Tested against the real database with real samples, including a genuine peak-fit failure handled correctly (flagged, not hidden)
Standalone interactive tool
  Live sensitivity adjustment, per-peak accept/reject — a quick, direct check outside the main app
Alloy Lab Database — Stage 2
2

## Slide 4
VSM — Complete
Full pipeline: instrument detection, mass extraction, segmentation, Hc/Mr, temperature coefficients, entropy change (ΔSm), demagnetizing correction + BHmax
  Two real segmentation bugs found and fixed during validation (turning-point false segments; a masking bug that hid a real 60K temperature jump)
  A real ~2× ambiguity in the demagnetizing-factor formula resolved through careful back-and-forth, not guessed
Database schema + real production integration
  Tested end-to-end against real data; 3 further real bugs caught and fixed along the way
Standalone interactive tool
  Full multi-segment file handling, adjustable sensitivity, per-segment accept/reject
Alloy Lab Database — Stage 2
3

## Slide 5
SEM — Real Progress, Real Challenge
Solved: three real instrument formats (Zeiss, JEOL, Tescan) — metadata, calibration, and databar cropping unified into one interface
  Grain detection validated on 16 real images; correctly flagged 2 deliberately low-quality images rather than forcing a confident wrong answer
The open problem: phase-fraction thresholding
  A simple automatic threshold worked on one real image and failed — differently — on two others
  One “failure” turned out to be real physical structure (confirmed via a second technique), not noise
Conclusion — with new/unfamiliar alloys, there is often not enough prior information to fully automate this step
  Resolution: automate what is reliably automatable; keep the phase judgment with the operator, via a live threshold tool
Alloy Lab Database — Stage 2
4

## Slide 6
Cross-Cutting Work
Standalone interactive tools
Built on the same validated analysis code as the database pipeline — not a separate re-implementation
Same working pattern each time: automate the reliable parts, keep human judgment where it genuinely belongs
Quick sample checks, outside the main app, no database writes
Database and element-fraction table
Real atomic-percent composition data backfilled and validated against real samples
Wide-format “composition vector” reshaping — the shape ML tooling will eventually need
Project reorganization (stage boundaries, shared config) completed cleanly, including catching and recovering from a real near-miss during the process
Alloy Lab Database — Stage 2
5

## Slide 7
Open Questions / Remaining Work
SEM
  Phase-fraction tool built — needs use on real samples to see if the manual-judgment approach holds up in practice
  16-bit instrument data (Tescan) handled for phase fraction; grain-detection tool not yet re-tested on it
  Kerr microscopy and EBSD — deliberately parked as their own future topics
Database
  Element-fraction table: automatic wiring into new-sample entry — deferred to end of Stage 2
  Inventory table — deferred to end of Stage 2
Other instruments
  Lakeshore VSM, Metis magnetometer — not yet started, lower priority
Alloy Lab Database — Stage 2
6

## Slide 8
Why This Approach
Automation earns its place where it is genuinely reliable. Where judgment is still required — new materials, ambiguous contrast, unfamiliar geometry — the tool should say so, not guess.
Every physics-facing module validated against a certified standard or known real data before use (LaB6 for XRD; multiple independent real-data cross-checks for VSM)
Real, silent-failure risks caught by testing, not assumed away — a demagnetizing-factor mix-up would have been a confidently wrong answer, off by roughly 2×, with nothing in the output to flag it
SEM phase-fraction: a plausible-looking automatic answer was wrong on 2 of 3 real images — for two different reasons — and only caught because a person looked
Every tool built this way: automate the reliable steps, put a live control in the operator's hands for the judgment calls
Alloy Lab Database — Stage 2
7

## Slide 9
Autonomous Labs: Optimization vs. Discovery
“Discovery Loop” (a well-funded, recently launched AI startup): full automation of the research cycle — hypothesis, experiment, analysis — across scientific domains, “without constant human intervention.”
Autonomous optimization
Known material, known phase space
Refining synthesis/processing conditions
A wrong step is cheap to detect and correct
Genuinely achievable today (CAMEO, A-Lab, and similar systems)
Autonomous discovery
New or under-characterized material
No ground truth to check the answer against
A wrong step can be silent and plausible-looking
This project's own experience: real, human-caught examples this stage
Alloy Lab Database — Stage 2
8

## Slide 10
Where This Leaves Us
XRD and VSM: fully built, validated, and integrated
SEM: real progress, with the hard part correctly identified as needing human judgment, not more automation
A consistent, tested philosophy across all three: automate what's reliable, keep a human in the loop where it isn't
Alloy Lab Database — Stage 2
10